## Slide 1: Inducing e.m.f and Current Generators and Transformers

## Slide 2
Faradays Law Lenz’s Law Review
Generators
Transformers

## Slide 3: Review – Some Important Laws
What can you remember about….
Faradays Law?
Lenz’s Law?

## Slide 4: Faraday’s law
The induced e.m.f. is equal to the rate of change of magnetic flux,
e.m.f = -ΔФ
Δt

## Slide 5: Lenz’s Law
Heinrich Lenz 1833
If an induced current flows, its direction is always such that it will oppose the change which produced it

## Slide 6: Eddy Currents - Demo
Two metal plates are setup on a pendulum as shown. Both are the same size and square, but one plate has grills cut through it.
Predict the outcome as both are swung through the magnetic field.

## Slide 7: Eddy Currents - Demo
The square plate swings through the field but is slowed by an induced current as explained by Lenz’s law.
We refer to that current as an eddy current. Eddy currents can produce significant drag, called magnetic damping, on the motion involved.
Another important fact about eddy currents is that they produce heat and result in energy loss.

## Slide 8: Eddy Currents - Demo
The direction of the eddy currents depends on whether the plate is swinging into or out of the magnetic field.
When the plate is swinging into the field a repulsive force is produced by the induced current.
When the plate is swinging out of the field an attractive force is produced by the induced current.

## Slide 9: Eddy Currents - Demo
The cut plate swings through the field with less dampening because the eddy currents formed are restricted in size by the forks of the conductor.
Furthermore, the individual eddy currents partially cancel each other out where fields of two eddy currents are in opposite directions.

## Slide 10: Laminated Iron – Recues Eddy Current Effects

## Slide 11: Review Question
Identical magnets A and B are suspended above vertical copper tubes as shown in the diagram
The magnets are dropped at the same time. Each magnet falls straight through its tube without touching the tube walls.
Which magnet leaves its tube first and why?

## Slide 12: Alternating Current Generators
Most electricity is produced using the ‘generator effect’.
This includes:
Coal and gas power,
Nuclear power
Hydroelectric power,
Wind power etc….
The simplest generators and the types used in power stations produce alternating current (A.C.)

## Slide 13: Motor = Generator
If electric energy enters a motor it is changed into kinetic energy, but if kinetic energy is input (the motor is turned) electric energy is produced!

## Slide 14: Generator/dynamo
A generator works in this way by rotating a coil in a magnetic field (or rotating a magnet in a coil)

## Slide 15: Alternating current
A coil rotated in a magnetic field will produce an e.m.f.
N
S

## Slide 16: Alternating current
In the vertical position, the plane of the coil is perpendicular to the field, therefore it will cut maximum flux according to .
N
S
Ф = BA cosθ

## Slide 17: Alternating current
In the horizontal position, the plane of the coil is parallel to the field, therefore it will cut ZERO flux according to .
N
S
Ф = BA cosθ

## Slide 18: Alternating current
As the coil spins, the effective area that is perpendicular to the field lines is reduced according to a cosine function.
This also means that the rate at which the area changes is not constant (linear) and therefore e.m.f. is not constant. (Faraday’s Law)

## Slide 19: Alternating current
In the vertical position the flux cut by the coil is maximum.
Motion however is parallel to the field so current and e.m.f induced is ZERO.
e.m.f = lvB ┴

## Slide 20: Alternating current
In the horizontal position the flux cut by the coil is ZERO.
Motion however is perpendicular to the field so e.m.f induced is maximum.
e.m.f = lvB ┴
USE YOUR HAND RULES TO CHECK THAT CURRENT DIRECTION IS CORRECT

## Slide 21: Alternating current
At points in-between horizontal and vertical, the component of velocity perpendicular to the field decreases.
This means induced e.m.f. decreases too.
e.m.f = lvb

## Slide 22: Alternating current
The e.m.f. produced is sinusoidal (for constant rotation)
e.m.f.
V

## Slide 23
MAX area and FLUX
ZERO e.m.f.
ZERO area and FLUX
MAX e.m.f.

## Slide 24: Slip ring commutator
To use this e.m.f. to produce a current the coil must be connected to an external circuit using either a slip ring commutator (shown below) or a split ring commutator (like a motors).
Slip-rings
lamp

## Slide 25: Slip Ring Commutator vs. Split Ring Commutator
A split ring commutator will
Result in DC current output
(discussed later).
A slip ring commutator will
Result in AC current output.

## Slide 26: What happens if the frequency or rate of rotation is doubled?
e.m.f.
V
What did that Faraday guy say again?

## Slide 27: Moving Coil A.C. Generator
Daw arrows in to show the direction of current flow at this moment in both the coil and the wires leading to the meter.

## Slide 28: Review: Which terminal / end is positive at this moment in time?

## Slide 29: AC Generator Calculations – Average e.m.f.
A coil with an Area A and a number of turns N rotating with a frequency of f will have a change in flux of BA in one quarter of a full rotation. (this is from zero to maximum flux BA).
In a full rotation it will do this change 4 times, thus….
You can use this if you know the time of one complete rotation (period)
You can use this if you know the time for one quarter of a rotation

## Slide 30: AC Generator Calculations – Average e.m.f.
Often information about generators states frequency of rotation instead of time as these are often very fast..
In which case we need to remember that
Average
Average

## Slide 31: AC Generator Calculations – PEAK or MAX e.m.f.
As can be seen from the graph, the e.m.f. induced varies significantly with time. Our power supply is rated at 240V but in fact has much higher voltages at the crests of the curves. The maximum e.m.f. can be calculated using the position where velocity perpendicular to the field is at its maximum.
Where is in a rotation is that?

## Slide 32: AC Generator Calculations – PEAK or MAX e.m.f.
Since the coil is rotation through a circle,
the distance covered in one rotation is equal to the circumference, and therefore the velocity is equal to
and therefore
L
r

## Slide 33: AC Generator Calculations – PEAK or MAX e.m.f.
But 2r = Diameter (which is the width of the coil) .
and Length x Diameter = Area of the coil so….(for each side)
Considering both sides and the number of turns the maximum e.m.f. becomes…
L
r

## Slide 34: Example 1
A coil with 120 turns measures 12.0 cm by 8.50 cm and rotates at 1200 rpm through a field of 0.150 T. What is the average e.m.f. that is generated?
F = 1200rpm
= 20 Hz
N = 120
A = 0.120 x 0.0850
= 0.0102 m2
B = 0.150 T
Average
Average
Average
Voltage varies between positive and negative e.m.f
so we usually drop the negative sign.

## Slide 35: Example 2
A coil with 120 turns measures 12.0 cm by 8.50 cm and rotates at 1200 rpm through a field of 0.150 T. What is the Maximum e.m.f. that is generated?
F = 1200rpm
= 20 Hz
N = 120
A = 0.120 x 0.0850
= 0.0102 m2
B = 0.150 T
Max
Max
Max
Voltage varies between positive and negative e.m.f
so we usually drop the negative sign.

## Slide 36: Root mean square voltage and current
It is useful to define an “average” current and voltage when talking about an a.c. supply.
Unfortunately, the average voltage and current is zero!
To help us we use the idea of root mean square voltage and current.

## Slide 37
e.m.f.
V
Root mean square voltage

## Slide 38: Root mean square voltage
First we square the voltage to get a quantity that is positive during a whole cycle.
e.m.f.
V

## Slide 39
Then we find the average of this positive quantity
e.m.f.
V
Root mean square voltage

## Slide 40: Root mean square voltage
We then find the square root of this quantity.
e.m.f.
V

## Slide 41: Root mean square voltage
We then find the square root of this quantity.
e.m.f.
V
This value is called the root mean square voltage

## Slide 42: Root mean square voltage
We then find the square root of this quantity.
e.m.f.
V
Erms = Emax
√2
Emax

## Slide 43: Example 3
What is the RMS e.m.f. induced by the coil in example 1 and 2
Max

## Slide 44: Bicycle generator
When the wheel turns the magnet is made to rotate next to the fixed coil of wire.
Electromagnetic induction occurs and a alternating voltage is induced in the coil.
This causes an alternating current to flow to the light bulb of the bicycle.

## Slide 45: DC Generator

## Slide 46: Review Question
The graph opposite shows how the voltage of an AC generator varies in time.
Describe or draw show how the voltage would vary if …..
Rotational frequency is halved
Area of the coil in the field is doubled
A split ring commutator was used instead of a slip ring commutator.
V
time

## Slide 47: The transformer
A transformer is a device that is used to change one alternating voltage level to another.
circuit symbol

## Slide 48: Structure of a transformer
A transformer consists of at least two coils of wire wrapped around a laminated iron core.
laminated iron core
PRIMARY VOLTAGE Vp
PRIMARY COIL of Np turns
SECONDARY COIL of Ns turns
SECONDARY VOLTAGE Vs

## Slide 49
Explanation:
B-field due to growing primary I
primary coil
secondary coil
(like an approaching magnet)
B-field ‘cuts’ in secondary coil
induced I opposes the build-up of
B-field
growing B-field due to induced I in secondary coil
Mutual inductance

## Slide 50: Mutual inductance
steady B-field due to steady primary I
primary coil
secondary coil
B-field  to 0 as
secondary I  to 0
steady B-field
 no induced voltage
 secondary I  to 0

## Slide 51
When the switch is open…
B-field collapses when primary I is absent
Mutual inductance

## Slide 52
B-field due to induced I in secondary coil
By Lenz’s
Law
B-field collapses when primary I is absent
Mutual inductance
tries to oppose the retreat of the B-field

## Slide 53
Lastly, no B-field from primary I
B-field due to induced I in secondary coil collapses
Mutual inductance

## Slide 54
Mutual inductance

## Slide 55: Explaining How a transformer works
When an alternating voltage, Vp is applied to the primary coil of Np turns it causes an alternating current to flow in this coil.
This current causes a changing magnetic field in the laminated iron core which cuts across the secondary coil of Ns turns.
Electromagnetic induction occurs in the secondary coil due to the change in flux.
As the current direction in the primary coil reverses, so does the flux and…
this results in alternating current / voltage, Vs in the secondary coil so that the direction always opposes the change in flux.

## Slide 56: Step-up transformers
In a step-up transformer the voltage across the secondary coil is greater than the voltage across the primary coil.
The secondary turns must be greater than the primary turns.
Use: To increase the voltage output from a power station from 25 kV (25 000 V) to up to 400 kV.

## Slide 57: Step-down transformers
In a step-down transformer the voltage across the secondary coil is smaller than the voltage across the primary coil.
The number of secondary turns must be smaller than the primary turns.
Use: To decrease the voltage output from the mains supply from 230V to 5V to power and recharge a mobile phone.

## Slide 58: Review Question
Why can a transformer not change the level of the voltage output of a battery?
  A battery has a constant potential difference causing current to flow in one direction only.
  This current would produce a stable magnetic field in the iron core.
  This would therefore NOT cause electromagnetic induction in the secondary coil as there is no change in flux (Faraday’s Law).
  There would therefore be no secondary current or voltage.

## Slide 59: The transformer equation
The voltages or potential differences across the primary and secondary coils of a transformer are related by the equation:
primary voltage = primary turns
secondary voltage secondary turns
Vp = Np
Vs Ns

## Slide 60: Example 1
Calculate the secondary voltage of a transformer that has a primary coil of 1200 turns and a secondary of 150 turns if the primary is supplied with 230V.
Vp = Np
Vs Ns
230 / Vs = 1200 / 150
230 / Vs = 8
230 = 8 x Vs
230 / 8 = Vs
Secondary voltage = 28.8 V

## Slide 61: Example 2
Calculate the number of turns required for the primary coil of a transformer if secondary has 400 turns and the primary voltage is stepped up from 12V to a secondary voltage of 48V.
Vp = Np
Vs Ns
12 / 48 = Np / 400
0.25 = Np / 400
0.25 x 400 = Np
Primary has 100 turns

## Slide 62: Complete:
PRIMARY |  | SECONDARY | 
Voltage | Turns | Voltage | Turns
230 V | 1000 | 11.5 V | 50
230 V | 500 | 46 V | 100
230 V | 200 | 920 V | 800
9 V | 120 | 72 V | 960
Answers
50
46 V
200
9 V

## Slide 63: Transformer power transfer equation
If a transformer is 100% efficient then the power input to the primary coil is equalled by the power output from the secondary coil.
as power = current x voltage P = VI
Power Input = Power Output
then:
Ip x Vp = Is x Vs

## Slide 64: Example 3
Calculate the primary current when a transformer is supplied with 230V the secondary provides 4A at a voltage of 13V. Assume that the transformer is 100% efficient.
Ip x Vp = Is x Vs
Ip x 230V = 4A x 13V
Ip = 52 / 230
Primary current = 0.226 A

## Slide 65: Example 4
Calculate the secondary current from a transformer supplying a secondary voltage of 6V if the primary is supplied with a current of 0.20A at 230V. Assume that the transformer is only 95% efficient.
Pp x 95% = Ps
Ip x Vp x 0.95 = Is x Vs
0.2A x 230V x 0.95 = Is x 6V
Is = 43.7 / 6
Secondary current = 7.28 A

## Slide 66: Complete:
PRIMARY |  |  | SECONDARY |  | 
Np | Vp | Ip | Ns | Vp | Is
600 | 200V | 0.4 A | 30 | 10V | 8 A
100 | 12V | 8 A | 4000 | 480V | 0.2 A
300 | 72V | 0.4 A | 50 | 12V | 2.4 A
50 | 25V | 10 A | 250 | 125V | 2 A
Answers
1
2
4
5
3
6
7
8

## Slide 67
At power stations the output voltage of the generators is stepped up by transformers from 25kV to 132kV.
The voltage may be further increased to up to 400 kV for transmission over long distance pylon lines.
Power transmission

## Slide 68
The voltage is reduced in stages by step-down transformers to different levels for different types of consumer.
The lowest level is 230-240V for domestic use. The final step-down transformer will be at sub station within a few hundred metres of each group of houses.
Power transmission

## Slide 69: Why do we Step up and Step down Voltage for Power transmission?
The higher the voltage used, the greater the efficiency of energy transmission is. (i.e less energy loss). Thus we step up voltage for transfer of power over long distances.
Step-up
Step-down
Step-down
15,000 V
250,000 V
11,000 V
240 V

## Slide 70: Why do we Step up and Step down Voltage for Power transmission?
Lower voltages result in higher electric currents and greater energy loss to heat due to the resistance of the cables.
Step-up
Step-down
Step-down
15,000 V
250,000 V
11,000 V
240 V

## Slide 71: Why do we Step up and Step down Voltage for Power transmission?
Voltage is only reduced to low values when very close to the delivery point..
Step-up
Step-down
Step-down
15,000 V
250,000 V
11,000 V
240 V

## Slide 72: Power transmission – Energy Loss Calculations
When current passes through a wire, the power dissipated (lost as heat or other energy types) is equal to
P = VI across the wire
Since V = IR
Power dissipated (loss) = I2R

## Slide 73: Power transmission
Power dissipated = I2R
Since the loss of power depends on the square of the current, when transmitting energy over large distances it is important to keep the current as low as possible.
However, to transmit large quantities of energy we therefore must have a very high voltage.
Power = Work / Time

## Slide 74: Power loss and Voltage Drop Example Calculations
300 MW of electricity is transmitted at 250 kV, along a 250 km long power line with resistance of 1.00 ohm.
What is the output voltage at the other end of the power line?
W
Calculate Current Flowing in Lines
Calculate Power Loss in Lines
Calculate Power Output at End of Line
Calculate Reduced Potential at end of Line
How would these values change if the power was transmitted at 50 kV? Try the calculation now.