## Slide 1: Translational Equilibrium

## Slide 2: Translational Equilibrium
For a rigid body to be in TRANSLATIONAL equilibrium, the sum of the forces must be zero
What did Newton say about that?

## Slide 3: Translational Equilibrium
.
How do the downward forces T1, compare to T2? When there is no acceleration.
How do the two tensions T1, compare to T2?
Conclusion: apart from changing the direction of the required force, this pulley does not change the force required to lift the bucket.

## Slide 4
Translational Equilibrium
F = L
(pulley changes
direction only)
F = ½ L
(pulley divides force)
P = ½ W
(moveable pulley divides force, second changes direction only)

## Slide 5: Simple Translational Equilibrium Problems
Bob the window cleaner has had a few too many cheeseburgers.
His weight is 1100 N, whilst Mark weighs only 710 N. The tension on the cables holding Mark’s side of the platform is 860 N. What is the tension on Bob’s side?
1100 N
710 N
860 N

## Slide 6: 2 D Hanging Problem 1
A traffic light set is hung from 2 cable attached to a pole as shown. The Traffic lights have a mass of 20.0 kg. What is the tension in each of the two cables?
30⁰
60⁰
= 20 x 9.8
196N
NOTE – Force is not necessarily proportional to length of the cables.

## Slide 7
Two cables hold a sign from a support as shown. If T1 has a tension of 260N, what is the mass of the sign?
2 D Hanging Problem 2
30⁰
60⁰

## Slide 8: Other possible situations

## Slide 9
An Olympic gymnast lifts his 65.0 kg body mass on the rings using the strength of his arms as shown. Each arm is angled downwards 10.0 degrees from horizontal. What is the force directed up each arm from the rings?
2 D Hanging Problem 3
10⁰
10⁰
637N
20⁰
80⁰