## Slide 1: Moments – Rotational Equilibrium
Doing well in Physics is a “Balancing Act”.

## Slide 2: Today’s lesson
Know the principal of moments.
Apply to Rotational Equilibrium problems.
for a rigid body to be in equilibrium, the sum of the forces and the sum of the moments must be zero
This looks harder than it actually is.

## Slide 3: Equilibrium
For a rigid body to be in static equilibrium, the sum of the forces and the sum of the moments must be zero

## Slide 4: Principal of Moments
Rotational equilibrium is when the sum of the anticlockwise moments equal the sum of the clockwise moments.

## Slide 5: Equilibrium - More than one force
Take an uneven see-saw for an example
Yo Kim!
Do you think we’ll be safe in this power point?
It’s not looking good Kanye!
pivot

## Slide 6: If the see-saw is balanced, what must be Kanye’s weight?
pivot
1.2 m
2.2 m
637 N
? N

## Slide 7: The force on the left is trying to turn the see-saw anticlockwise about the pivot
pivot
1.2 m
2.2 m
? N
637 N

## Slide 8: The force on the right is trying to turn the see-saw clockwise about the pivot
pivot
1.2 m
2.2 m
? N
637 N

## Slide 9: If the see-saw balances, the turning effect anticlockwise must equal the turning effect clockwise
pivot
1.2 m
2.2 m
? N
Anticlockwise moment
clockwise moment
=
637 N

## Slide 10: Anticlockwise moment = clockwise moment ∑ACM = ∑CM r F = r F 1.2 x Fw = 2.2 x 637 1.2 x Fw = 1401.4 ? = 1401/1.2 Fw = 1.17 x 103 N
pivot
1.2 m
2.2 m
? N
Anticlockwise moment
clockwise moment
=
637 N
You fat little piggy!

## Slide 11
Phew! We seemed to have survived the PowerPoint!
pivot

## Slide 12
Don’t speak too soon!
pivot
BOMB

## Slide 13
pivot
BOMB
. Yo, Kim, I'm really happy for you, I'ma let you finish, but…

## Slide 14
pivot
BOMB

## Slide 15
pivot
BOMB

## Slide 16
pivot

## Slide 17
pivot
Nice one!

## Slide 18: The Combined Turning Effect of Multiple Forces
What force does the bicep muscle need to apply to hold the mass?

## Slide 19: The Combined Turning Effect of Multiple Forces
60o
70 kg
W
5 m
3 m
What is the counterweight (W) required to balance the light crane arm shown in diagram ?

## Slide 20: The Combined Turning Effect of Multiple Forces
What is the tension (T) in the cable shown in diagram?
T
25 m
20 m
65o
70 N

## Slide 21: The Combined Turning Effect of Multiple Forces
What is the tension (T) in the cable shown in diagram?
20 N
3 m
1.5 m
T
70o

## Slide 22: The Combined Turning Effect of Multiple Forces
To calculate angle
therefore third angle = 149.5
Therefore Fr = 37.6N @ 59.5 down from horizontal
20 N
3 m
1.5 m
T
70o
There is a third force in this situation, provided by the reaction force from the wall at the pivot.
What is the size and direction of this force?
20o
θ

## Slide 23: Any Questions?

## Slide 24
pivot
You’ll have to do some problems now, or he’ll kill me too!

## Slide 25
pivot
Hurry up … Open your books!
Static Equilibrium – Chapter 3.3

## Slide 26: ATAR / WACE exam questions
2010 Q’s 2, 19
2011 Q’s 8, 10
2012 Q’s 5, 9 (v Difficult)
2013 Q’s 5.
2014 Q’s 13, 16
2015 Q’s 4, 15
2016 Q 18.
2017 Q 6, 9, 11 (hard),