## Slide 1: Turning Effects of Forces
Can we torque about this?

## Slide 2: Today’s lesson
Know what the turning effect of a force is
Know that the moment of a force depends on force and the distance from the pivot
when an object experiences a net force at a distance from a pivot and at an angle to the lever arm, it will experience a torque or moment about that point
Something funny is going on here??

## Slide 3: What happens when you try to open a door with one finger?
Where do you push?
Hi, my name is Mr Stick
hinges

## Slide 4: Do you push near the hinges?
I can’t do it!

## Slide 5: Do you push far from the hinges?
That’s easier!

## Slide 6: The turning effect of a force depends on two things;
The size of the force
Obviously!

## Slide 7: The turning effect of a force depends on two things;
The distance from the pivot (axis of rotation)
Not quite so obvious!
Axis of rotation

## Slide 8: To get the same turning effect closer to the hinge, a larger force is required

## Slide 9: Turning effect of a force
The turning effect of a force is called the moment of the force.
It is also commonly known as Torque
The moment is calculated by multiplying the force (perpendicular to the pivot) by the distance from the pivot

## Slide 10: Turning effect of a force – moment of a force or TORQUE
Moment (torque) (Nm) = distance from pivot (m) x Force (N)
Note the unit is Nm, not N/m!
This assumes that the Radius and the Force are perpendicular to each other.
If they are not then the perpendicular component must be used. (thus the sin θ)

## Slide 11: A simple example!
nut
spanner (wrench)
50 N
0.15 m

## Slide 12: A simple example!
nut
spanner (wrench)
50 N
0.15 m
Torque = 0.15 x 50 x sin 90
Torque = 7.5 Nm

## Slide 13: What do you do if the nut won’t move and you can’t push harder?!
nut
spanner (wrench)
50 N
0.15 m

## Slide 14: Get a longer spanner!
nut
spanner (wrench)
50 N
0.25 m
Moment = Force x distance from pivot
Moment = 50 N x 0.25 m
Moment = 12.5 Nm

## Slide 15: Moments – Turning forces
A longer lever arm is very helpful in rotating objects.

## Slide 16: Moments – Turning forces
Sometimes levers can reduce the size of the force required, whilst others increase the distance or speed of movement instead.

## Slide 17
Moments - Effect of Angles
What is the significance of this diagram ?
X shows the perpendicular distance
from the pivot to the line of force.
This is important because torque is the product of the force and the perpendicular distance to the line of its action.
Alternatively the component of the force perpendicular to the radius.

## Slide 18
Moments - Effect of Angles
How could the the perpendicular distance from the pivot to the line of force be calculated?
Radius = r
θ = 40⁰

## Slide 19
Moments - Effect of Angles
Alternatively we could find the component of the force that is perpendicular to the radius.
40⁰
Fp

## Slide 20
Radius = r
θ = 40⁰
Moments - Effect of Angles
Two methods Same Solution.
40⁰
Fp

## Slide 21
Moments - Effect of Angles
Example: The length of a bicycle pedal arm is 0.152 m, and a downward force of 111 N is applied by the foot.
What is the magnitude of torque about the pivot point when the angle θ between the arm & vertical is: 30.0° (as shown) 90.0° (i.e. pedal at right angles) and 180° (i.e. straight down)
30.0° t = 0.152 x 111 x sin 30.0° = 8.44 Nm
90.0° t = 0.152 x 111 x sin 90.0° = 16.9 Nm
180.0° t = 0.152 x 111 x sin 180.0° = 0 Nm

## Slide 22: What method you use depends on the information provided in the question.

## Slide 23: Moments – Chapter 3.1
No dogs were harmed in today’s presentation, but just to be on the safe side ..
You better get working NOW!!